## Slide 1: Push Services for UMOBILE
UCAM

## Slide 2: Push vs Pull Communication Models
Producer
Consumer
Content/Service
Request content/service
Pull Model
Producer
Consumer
Content/Service
Push Model
Consumer initiates the communication by sending the request towards publisher
This model is natively supported by NDN
Producer takes control the content and sends content/service to consumer (e.g., sending the notification)
This model is not inherit supported by NDN

## Slide 3: Data forwarding in NDN
Data Delivery is based on
“reverse path forwarding”
  Producer cannot directly send Data to Consumer
  Forwarding Data message follows information in the PIT.
  PIT entry is registered when Interest message is flowed to NDN node.
Name Prefixes | Face
/umobile/emergency | A
Data:
/umobile/emergency/info
Name Prefixes | Face
/umobile/emergency | A
A
B
A
B
“Need Interest message to create an PIT entry”

## Slide 4: Communication Models in UMOBILE
As mentioned in UMOBILE ICN layer abstraction initial specification (D3.3), UMOBILE platform requires both Push and Pull communication models
Applications | Communication Models | Context Services | Data Services
Recommendation (shopping, parking) | Pull | Recommendations | Data dissemination Data filtering
Local News (art exhibitions; road accidents)) | Push/Pull | Affinity networks Recommendations | Data dissemination Data filtering (end-user device)
Chat | Pull | Affinity networks | Data dissemination Data synchronization
Instant messaging (send info to any authorities: fire); | Push | Behavior inference | Data dissemination
Emergency channel (e.g. info about safety places) | Push | Affinity networking | Data dissemination Data pre-fetching Data synchronization

## Slide 5: Proposed Push based Communication Models
Proposed 3 approaches to implement the Push based communication models (D3.1)
Build models based on primitive Interest/Data exchange of NDN
  Controlling the entry (Push Interest) in PIT table
  Timeout of PIT entry (Push Interest) must be short
  Implemented through PyNDN
Interest Polling
Interest Notification
Publish Data Dissemination

## Slide 6: Interest Polling
Consumer
Data Producer
Content is not always available
Consumer keeps polling the producer
Applicable scenarios
  Emergency situation
    The connectivity is intermittent
  IoT
    The producer (e.g., sensors) takes sleep mode to save the energy
Interest
Interest
Interest
Data
Content becomes available, Producer replies with Data message

## Slide 7: Interest Notification
Consumer
Data Producer
Content is generated as string format (e.g., instance message, text notification)
Content is appended to the Interest name
Applicable scenarios
  Sending instant message
  Sending emergency notification
Interest
Data
Ack Data
(Optional)
/umobile/emergency/<Data>
An example of Interest message used in Emergency scenario

## Slide 8: Publish Data Dissemination
Consumer
Data Producer
Interest: name/pub)
Interest: /name
Data: /name/chunk1
Interest: name/chunk2
Data: /name/chunk2
Interest: name/chunk N
Data: /name/chunk N
Content cannot be attached to Interest name (e.g., file.tar)
Producer publish their contents or services via Interest message
Subscribed consumer sends back Interest messages to fetch Data.
Applicable scenarios
  Service migration (WP4)

## Slide 9: Evaluations of Push Services
Interest Polling
Interest Notification
Publish Data Dissemination
Evaluated through NDN Smart Lighting System[1]
[1] U. Silva, A .Lertsinsrubtavee, A. Sathiaseelan, K. Kanchanasut, “Named Data Networking Based Smart Home Lighting” ACM SIGCOMM Poster, 2016.
Evaluated through service migration (WP4)