## Slide 1: KEBAPP Keyword-Based Mobile Application Sharing Framework
Dr Ioannis Psaras
EPSRC Fellow
University College London
Email: i.psaras@ucl.ac.uk
Web: http://www.ee.ucl.ac.uk/~ipsaras/
Paper available at: http://www.ee.ucl.ac.uk/~ipsaras/kebapp-mobiarch16.pdf
I. Psaras et al. “Keyword-Based Mobile Application Sharing”
Best Paper Award
@
MobiArch 2016
Work done together with Sergi Rene, Vasilis Sourlas, Dinos Katsaros and George Pavlou (UCL)
and Ioannis Komnios, Sotiris Diamantopoulos, Nikos Bezirgiannidis, Vasilis Tsaoussidis (DUTH, GR)

## Slide 2: What is KEBAPP – Contribution
Route Finder App
Game or Video-Streaming Server
Super Boring!
HELP!
An application sharing and information-processing framework for smartphone apps
Notes: <number>

## Slide 3: What applications does KEBAPP deal with (Design Space)
By and large, smartphone apps target:
  Static content, e.g., news updates
  Personalised content, e.g., Facebook/Twitter updates
  Processed information, e.g., route finder, gaming
We envision a pool of application resources to provide D2D access to processed and non-personalised information

## Slide 4: Where/When do we need KEBAPP (Target environments)
Overcrowded areas
  Airports, festivals, stadiums, IETF :)
Fragmented networks
  Natural disasters (floods, earthquakes)
Not (or poorly) connected environments
  Airplanes, trains, ferries, developing regions
In most of those cases, Internet connectivity is not even necessary!

## Slide 5: How does KEBAPP work?
Three main components
Application-centric naming
  Applications share common name-spaces and support the use of keywords
Application-centric connectivity
  Applications manage connectivity by defining and/or joining WiFi broadcast domains
Information-centric forwarding
  Extending Named Data Networking
  primitives
Applications act both as clients and as servers

## Slide 6: Application-Centric Naming (App IDs)
Needs to support fine-grained description of the desired processed information
Fixed part: NDN hierarchical naming, longest prefix match
  Needs to guarantee compatibility between applications
  Can define static content: /NewsApp/politics/
  Or invoke computation: /myTravelAdvisor/Top10Restos
  App GUI indicates naming, users do not have to be aware of naming
Hashtags: free keywords to assist application processing
  /myTravelAdvisor/Top10Restos #userRating; #London; #indian
  /routeFinder/tube #euston; #waterloo
Notes: <number>

## Slide 7: Application-Centric Connectivity
Application-specific 802.11 broadcast domains, through Basic Service Set(s), BSSs
  Every KEBAPP advertises its own SSID, through WiFi Direct Groups
  WiFi Neighbour-Awareness Networking (NAN) can find applications behind BSSs
gameX
tripAdvisor
routeFinder
*K.V. Katsaros et. al. “Information-Centric Connectivity”,
IEEE Communications Magazine, to appear.

## Slide 8: Information-Centric Forwarding
Single-hop broadcasting domains
Broadcast domains are considered as interfaces of a node
FIB is populated with neighbouring BSSIDs
gameX
tripAdvisor
routeFinder
Name Prefix | BSSID | if
/travel/tripAdvisor #x #y | tripAdvisor | #1
/gaming/gameX #z | gameX | #2
Name Prefix | BSSID | if
/travel/routeFinder #x | routeFinder | #1

## Slide 9: Feasibility – RouteFinder App
Setup
Mobility trace from 3300 users in a Stockholm
subway station throughout one hour
All users: 3300
KEBAB
Users (10%)
RouteFinder
App Users

## Slide 10: How to implement KEBAPP?
Android implementation components
KEBAPP Application Activity
KEBAPP Application Service
KEBAPP Application Model
KEBAPP Application
KEBAPP framework
jndn (java libs)
WiFiDirect libs
jndn-manager
Naming / partial matching functions
Application model / functionalities
KEBAPP background service
KEBAPP Foreground app UI
NFD<->WiFiDirect interface
NDN
tables / routing / fwd options
Service discovery / connectivity
Network devices
KEBAPP APP software
KEBAPP middleware
Android OS
NFD

## Slide 11: Kebapp Implementation: Android
KEBAPP Applications (sockets vs process-content)
Two option for KEBAPP socket impl:
Generic API: KEBAPP framework is the responsible to choose either how to access the information (through the server or in using through KEBAPP).
KEBAPP socket API only: up to the application to use the “KEBAPP socket” or the normal socket depending on the functionality implemented in the application.
KEBAPP Application Activity
KEBAPP Application Activity
INET Socket
KEBAPP
Socket
NFD/NDN
IP
API
802.11
UMTS/LTE
WifiDirect
IPC:
Inter-process
Communication
PCC:
Process-Content
Communication
User space
Kernel space

## Slide 12
Thanks!
Work done together with Sergi Rene, Vasilis Sourlas, Dinos Katsaros and George Pavlou (UCL)
and Ioannis Komnios, Sotiris Diamantopoulos, Nikos Bezirgiannidis, Vasilis Tsaoussidis (DUTH, GR)